BF4L913 DIESEL ENGINE TECHNICAL DATASHEET

| MODEL OF DIESEL ENGINE | BF4L913 |
| --- | --- |
| NUMBER OF CYLINDER | 4 |
| NUMBER OF STROKE | 4 |
| COOLING WAY | AIR-COOLED |
| RATED POWER (KW/RPM) | 47/1500 |
|  | 55/1800 |
|  | 66/2300 |
|  | 78/2500 |
| CHAMBER TYPE | DIRECT INJECTION |
| BORE/STROKE(mm) | 102/125 |
| DISPLACEMENT(L) | 4.086 |
| AUTOMOTIVE POWER AS PER DIN70020 (kW(PH)/r/min) | 78(106)/2500 |
| ISO 3046/(IFN )NET BRAKE FUEL STOP POWER (kW(ps)/r/min) | MAX POWER HIGHLY INTERMITTENT | 78(106)/2500 |
|  | MAX POWER INTERMITTENT | 72(98)/2500 |
| ISO STANDARD FUEL STOP POWER (ICFN) | kW(PH)/r/min MAX | 66(90)/2300 |
|  | kW(PH)/r/min MIN | 47(64)/1500 |
| MAX.YORQUE AS PER DIN70020 (N.m/r/min) | 342/16500 |
| NET WEIGHT(kg) | 350 |
| DIESEL ENGINE SUPPORT SPACE(Dmm) | 575 |
| TYPE OF STANDARD FLYWHEEL CASING(SAE) | 2+3+4 |
| STARTING WAY | ELECTRIC |
| LUBRICATING WAY | PRESSURE LUBRICATION |
| ROTATION DIRECTION | COUNTER-CLOCKWISE |
| NET DIMENSION(L×W×H)(mm) | 725×665×800 |